## Slide 1
Foundations of
Manufacturing
Domain 1: Safety Awareness
Section 3: Walking Working Surfaces
Notes: This presentation is designed to assist trainers conducting OSHA 10-hour General Industry outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of 1970 or for any standards issued by the U.S. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the U.S. Department of Labor.

## Slide 2: Learning Objectives
OSHA, Walking and Work Surfaces
  Examine the various work surfaces in the manufacturing plant.
  Identify OSHA Safety Programs for work surfaces.
  Describe employer and employee duties and responsibilities under OSHA.
  Discuss the hazards associated with slips, trips, and falls.
  Describe the importance of housekeeping efforts.
  Describe the Personal Fall Protection System.
  Discuss the proper use of ladders and elevated work surfaces
.

## Slide 3: Introduction CFR Part 1910 Subpart D Walking-Working Surfaces (§1910.21 to 1910.30)
Slips, trips and falls cause:
  the majority of general industry accidents
  15 percent of all accidental deaths
  more fatalities than all other causes but motor vehicles
OSHA’s standards for walking and working surfaces apply to all permanent places of employment, except where only domestic, mining, or agricultural work is performed
Notes: 29 CFR Part 1910 Subpart D
Walking-Working Surfaces (§1910.21 to 1910.30)

## Slide 4: Accident Statistics
Slips, trips, and falls account for:
  Falls on the same level were the second leading cause of workplace injuries in 2003
  $6.9 billion in annual health care costs
Slips and trips without falls result in:
  Head, neck and back strain
  Pulled muscles

## Slide 5: Common Warning and Hazard Signs

## Slide 6: OSHA Hazard Colors
The Occupational Safety and Health Act (OSHA) stipulates that industrial plants provide color coded safety equipment and hazard areas. The list identifies the OSHA-designated colors and their meaning.

## Slide 7: Slip and Trip Accidents
Head or back injuries
Cuts and bruises
Fractures
Pulled muscles
Death

## Slide 8: Slip Hazards
Stairs and inclines
Loose rugs and mats
Water, oil, and chemicals

## Slide 9: Housekeeping – Potential Hazards
First impressions?
7
9/44

## Slide 10: General Requirements Housekeeping
Workplaces must be kept clean, orderly, and sanitary.
Workroom floors must be maintained as clean and dry as possible.
Report spots on the floor that appear to be hazardous chemicals to your supervisor – Hazard Response Teams may need to be called in to clean up.
Notes: Some of the most frequently cited violations in Subpart D involve housekeeping [1910.22(a)].
Drainage must be maintained and gratings, mats or raised platforms must be provided where wet processes are used.
Every floor, working place and passageway must be kept free from protruding nails, splinters, holes, or loose boards to facilitate cleaning.

## Slide 11: Housekeeping
Clean up liquids.
Install absorbent or barriers around machinery that leaks.
Use warning signs or cones.

## Slide 12: Floor Mats
Use around machinery where liquids and debris are normally present
Should have holes and/or be absorbent
Compatible with chemicals in use
Have beveled and colored borders

## Slide 13: Foot Wear
Has soft rubber sole for slip resistance
Sole’s tread has channels
Does not make you invincible
Steel-toe may be required

## Slide 14: Employee Awareness
Pay attention to where you are going.
Adjust your stride according to the walking surface and conditions.
Make wide turns at corners.
Make sure you can see the floor when carrying items.
Employees with less than one year of experience are 40% more likely to be injured.
Industrial injuries must be reported to management immediately

## Slide 15: Trip Hazards
Obstructions in walkways
Damaged or uneven floor surfaces
Electrical cords and air hoses
Running
Poor lighting

## Slide 16: Preventing Trips
Pick up tools, materials, and trash.
Walk around obstructions.
Do not carry items that block your forward vision.
Watch placement of power cords.
Keep file drawers closed.
Clean up straps and bands.

## Slide 17: QUESTION
Who is responsible for housekeeping?
Everyone!!!
Notes: Question - Can you identify a specific tripping hazard you have noticed in your workplace?

## Slide 18: Hazards Associated with Falls
Unsafe ladders or stairs
Inadequate guardrails
Improper use of personal fall arrest systems
Openings in floors
Using ladders incorrectly

## Slide 19: Fall Prevention Guidelines
Inspect ladders
Guardrails in place
Fall arrest training and use
Signage for all floor openings, floor holes, floor level changes
Barriers around skylights
Wall opening protection

## Slide 20: Ladder Inspection
Rungs are in good condition and clean
Ladder locks function correctly
Ladder is non-conductive
Ladder’s feet are anti-slip
Notes: Question: What should you look for when inspecting a ladder?
Answers will vary, but should include:
Grease, oil, or other slippery substances on rungs, and hand rails
Broken, damaged, or rusted, ladder locks
Wear on ladder feet, stability of ladder

## Slide 21: Portable Ladders
Ladders used to gain access to a roof or other area must extend at least 3 feet above the point of support
Withdraw defective ladders from service and tag or mark "Dangerous, Do Not Use“
Never use ladders in a horizontal position as scaffolds or work platforms
Never use metal ladders near electrical equipment
21/44
Notes: 1910.25
1910.26
Maximum length: Stepladders – 20 ft, single-rung ladders – 30 ft., two-section rung ladders – 60 ft.
1910.26(a)(2)(iii)
Based on the nominal length of the ladder, each section of a multisection ladder shall overlap the adjacent section by at least the number of feet stated in the following:
______________________________________________________
|
Normal length of ladder (feet) | Overlap (feet)
____________________________________|________________
|
Up to and including 36 .............| 3
Over 36, up to and including 48 ....| 4
Over 48, up to 60 ..................| 5
____________________________________|_________________
Stepladders must be equipped with a metal spreader or locking device to securely hold the front and back sections in an open position.
All ladders must be inspected periodically, kept in good condition at all times, and must be free from sharp edges, splinters, oil grease, or other defects which would affect their use.
- Always place the ladder on secure footing and lock in place.
- Short ladders shall not be spliced together to make long ladders.
- The top of a regular stepladder shall not be used as a step.
- Always face the ladder when climbing or descending.

## Slide 22: Ladder Set-Up
Put it on a level surface.
Secure the bottom.
Angle the ladder properly (4:1).
Extend the ladder 3 feet/rungs above the upper landing.

## Slide 23: Ladder Angle Portable Rung and Cleat Ladders
Use at an angle where the horizontal distance from the top support to the foot of the ladder is ¼ the working length of the ladder (length along ladder between the foot and top support).
Notes: 1910.25

## Slide 24: Using the Ladder
Face the ladder.
Climb with both hands.
Use a tool belt or bucket hanger.
Keep your weight centered.
Do not stand on the top four rungs or top two steps.
Use the “3 point grip” rule.
Notes: NOTE:
Withdraw defective ladders from service and tag or mark "Dangerous, Do Not Use“
Never use ladders in a horizontal position as scaffolds or work platforms
Never use metal ladders near electrical equipment

## Slide 25: What’s Wrong With This?
Notes: No handrail – required for 4 or more risers
Too steep – no 1-4 ratio
Rung height may be suspect – 6-12 inches
Uniform rung height off at bottom
Probably will not support 1000 lbs minimum
Top step sticks out past step below it – trip hazard
Hand rail at top too low

## Slide 26: Fixed Ladders
Permanently attached to a structure, building or equipment
Cages or wells required if longer than 20 feet to a maximum unbroken length of 30 feet.
Ladder safety devices may be used on tower, water tank and chimney ladders over 20 feet in unbroken length instead of cage protection
Rungs not less than 6 inches or more than 12 inches.
Minimum distance between side rails is 16 inches
Notes: 1910.27
All fixed ladders must be inspected regularly and be maintained in a safe condition.
Preferred pitch in range of 75 to 90 degrees with horizontal.

## Slide 27: Stair Safety
Walk, do not run.
Use the handrails.
Inspect for slippery surfaces or damaged steps.
Do not put objects on steps.

## Slide 28: Stairways
Flights of stairs with four or more risers must have standard stair railings or handrails.
Notes: 1910.23(d)(1)
1910.23(e)(2)

## Slide 29: Stairway Floor Openings
Must be guarded by a standard railing on all exposed sides (except at entrance)
Notes: 1910.23(a)(1)

## Slide 30: Fixed Industrial Stairs
Treads must be slip resistant with uniform rise height and tread width
Must be able to carry 5 times expected load; minimum of 1000 pounds
Minimum width of 22 inches
Violation here – several steps bent and damaged
Notes: 1910.24
Applies to interior and exterior stairs around machinery, tanks and other equipment, and stairs leading to or from floors, platforms or pits.
Does not apply to stairs used for fire exit purposes, to construction operations, to private residences, or to articulated stairs, such as those on floating roof tanks.
Fixed industrial stairs are required for access to and from places of work where operations necessitate regular travel between levels.

## Slide 31: Open-Sided Floors and Platforms
Open-sided floors or platforms 4 feet or more above adjacent floor or ground level must be guarded by a standard railing (or equivalent) on all open sides, except where there is an entrance to a ramp, stairway, or fixed ladder
A toeboard is required when, beneath the open sides:
  persons can pass,
  there is moving machinery, or
  there is equipment with which falling materials could create a hazard
Unguarded Platform
Notes: 1910.23(c)(1)

## Slide 32: Floor Opening
An opening measuring 12 inches or more in its least dimension in a floor, platform, pavement, or yard, through which persons may fall.
Notes: 1910.21(a)(2)

## Slide 33: Guarding Floor Openings Definitions
Standard railing. Consists of top rail, mid rail, and posts. Height from the upper surface of top rail to floor level is 42 inches. Mid rail height is 21 inches.
Standard toeboard. 4 inches high, with not more than ¼-inch clearance above the floor.
Notes: 1910.23(e)(1) and (4)

## Slide 34: General Requirements Aisles and Passageways
Keep clear and move obstructions that could create a hazard
Mark permanent aisles and passageways
Aisles must be sufficiently wide where mechanical handling equipment is used
Use marked pedestrian aisles and pedestrian doors
Keep floors clean and dry at all times
DO NOT allow extension cords, air hoses, etc., to cross walkway
Use mirrors to control blind spots
Notes: 1910.22(b)

## Slide 35: Compressed Gases
Includes oxygen and acetylene
Must be stored upright
Must be capped
Must be chained in approved racks
Must be at least 20 feet or a solid barrier between stored oxygen and stored acetylene containers
Must be stored in well ventilated area away from heat sources

## Slide 36: Personal Fall Arrest System
Worker tied to anchorage point
Safety harness worn
Lanyard, lifeline, deceleration device
Anchor point withstands 5000 pounds
Workers must be thoroughly trained

## Slide 37: Warning Lines
Flat Slope Surface
34-39 inches above surface
Rope, wire or chain
Stanchions able to withstand 16 pounds force
Highly visible
DO NOT ENTER UNLESS SECURED WITH PFAS!
Cassowary

## Slide 38: Warning Rail/Guard

## Slide 39: Scaffolding General Requirements
Must be capable of supporting four times the maximum intended load
Do not alter or move while in use
Protect workers on scaffolds from overhead hazards
If higher than 10 ft., use guardrails, midrails and toeboards
Use wire mesh between the toeboard and guardrail if people work or pass underneath
Must be equipped with access ladder or equivalent
Notes: 1910.28
Damaged or weakened scaffolds must not be used.
A safe means must be provided to gain access to the working platform level through use of a ladder, ramp, etc.
Never work on scaffolds during storms, high winds, ice, or snow.
Always be aware of the hazards of overhead power lines when working on scaffolds.

## Slide 40: Guardrails
Barrier along an open edge
42 inch high with mid-rail
Toe board or kick plate
Withstand 200 pounds of side load force

## Slide 41: Scaffolding
Built/moved by competent persons
No bricks or blocks for support
Don’t drop anything from scaffold
Plumb, level and square

## Slide 42: Aerial Lifts
Vehicle-Mounted elevating & rotating lift
Manually Propelled elevating work platform
Boom-Supported elevating work platform
Self-propelled elevating work platform

## Slide 43: Lift Hazards
Hydraulic Failure
Outriggers misplaced
Worker not tied off (PFAS)
Sudden movement, fall
Power Lines

## Slide 44: Summary
Slips, trips, and falls constitute the majority of general industry accidents
OSHA’s standards for walking and working surfaces include requirements for housekeeping, guarding floor and wall openings and holes, industrial stairs and ladders
Keeping working surfaces clean, dry, and uncluttered can prevent many workplace accidents