## Slide 1: Domain 1: Safety Awareness
Section 4:
Fire Safety and Exit Routes
Foundations of
Manufacturing
Notes: Read Lesson Link aloud to students:

## Slide 2: Learning Objectives
Identify evacuation plans, exit routes, and hazards that hinder evacuation.
Describe the proper fire extinguishing agents to use on different classes of fires.
Discuss the four classes of fires, their prevention, and associated hazards.

## Slide 3: Learning Objectives (Cont’d.)
Examine training requirements and applicable standards relating to exits, fire extinguishers, and storage and handling of flammable and combustible materials.
Identify the requirements, elements of the applicable standards, and the written plan for emergency response.
Describe chemical hazards, exposure, burns, hazard identification, and their importance to emergency response teams.
Notes: Direct students to turn to Page 2-3-1 in their TBL Manufacturing Fundamentals, Unit 2: Safety Awareness, Module 3: Fire Safety and Exit Routes, Student Workbook and continue with the discussion.

## Slide 4: Introduction
Serious fires occur in 70,000 to 80,000 workplaces annually
100 employee deaths, 1,410 employees injured annually
$2 billion in property losses annually (2003-2008)
OSHA requires employers to meet standards to prevent workplace deaths and injury
Notes: Question: What should employers do to protect workers from fire hazards?
Answer: Train workers about fire hazards, and procedures for evacuation, use of firefighting equipment, equipment safety, etc.

## Slide 5: Locations of Fires
22%- Storage properties
19%- Business/Mercantile
19%- Outside or special properties
14%- Public Assembly (church, town hall)
26%- Other non-residential

## Slide 6: General Duty Clause
Employer must provide workplace free from recognized hazards
Employers must comply with OSHA, state and local standards for safety and healthful workplace

## Slide 7: Evacuation Plans and Exit Routes
  Employers’ responsibility to put evacuation plan in place
  Employees’ responsibility to understand and execute the plan
  Know where all emergency routes are located
  Path must be open all the time
  Two exit routes required
7/67

## Slide 8: Evacuation
Shut down equipment
Evacuate
Headcount
Keep fire exits clear
Annual drills

## Slide 9: Evacuation Preparedness
Keep evacuation organized.
Know your evacuation plans.
Train for and practice evacuation procedures.
Conduct ERT training within 30 days for new hires and then annually.

## Slide 10: Mock Tabletop Evacuation Drill
Responding to alarm
Evacuation roles and understanding them
Shut down critical equipment
Exit the area
Assemble promptly
Head count
Notes: Tabletop Exercise (TTX): A tabletop exercise involves key personnel discussing simulated scenarios in an informal setting. TTXs can be used to assess plans, policies, and procedures
Question: What are some important things to do during an emergency evacuation/evacuation drill?
Answer:
Keep fire exits clear.
Shut down and secure critical equipment.
Evacuate to designated assembly areas and wait for the head count.
Evaluate practice drills.
Discuss each answer further to ensure student understanding.
Question: Should a company have a different notification procedure for chemical spills?
Answers will vary.
Question: Does your company have distinctive alarms for specific emergencies? Example: One alarm tone indicates a local fire, a different tone indicates a chemical spill and another indicates the need for total evacuation.
Answers will vary.
Question: What evacuation procedure does your company have in place?
Answers will vary.

## Slide 11: QUESTION
An emergency alarm just went off. You should:
Initiate emergency shut down procedures and evacuate

## Slide 12: Emergency Drills and Incidents
Record the overall status of any drills that take place
Document any incidents that occur
12/67

## Slide 13: Exit Route (Egress)
A continuous and unobstructed path of exit travel that is permanent and has enough exits for quick escape
Consists of three parts:
  Exit access
  Exit
  Exit discharge

## Slide 14: Exit Discharge
Must lead directly outside or to a street, walkway, refuge area, public way, or open space with access to the outside that is large enough to accommodate all building occupants likely to use the exit route
Exit stairs that continue beyond the level on which the exit discharge is located must be interrupted on that level by doors, partitions, or other effective means that clearly indicate the direction of travel to the exit discharge

## Slide 15: QUESTION
Why do we need to keep exit paths clear and doors closed?
Notes: A – for fire safety and containment

## Slide 16: Exit Door and Route Requirements
Doors remain unlocked
Must be able to open from the inside at all times without keys, tools, or special knowledge
A device such as a panic bar that locks only from the outside is permitted
Must be free of any device or alarm that could restrict emergency use if the device or alarm fails

## Slide 17: Exit Route Requirements
Support the maximum permitted occupant load for each floor served
Capacity must not decrease in the direction of exit route travel to the exit discharge
Ceiling at least 7 feet 6 inches high with no projection reaching a point less than 6 feet 8 inches from floor
Access at least 28 inches wide at all points

## Slide 18: Exit Marking Requirements
Each exit clearly visible and marked with an “Exit” sign
Each exit route door must be free of decorations or signs that obscure the visibility of the door

## Slide 19: Exit Markings Requirements (Cont’d.)

## Slide 20: Exit Markings Requirements (Cont’d.)

## Slide 21: Refuge Area
A space along an exit route protected from fire
May be a floor with at least two spaces separated by smoke resistance partitions

## Slide 22: Safe Escape Factors
Considerations
  Panic and confusion
  Poor visibility
  Lack of information or misinformation

## Slide 23: Emergency Action Plan
Emergency escape/evacuation procedures
Pre-evacuation procedures for critical operations
Post-evacuation employee accountability procedures
Rescue/medical duties
Fire/emergency reporting procedures
Contacts for further plan information

## Slide 24: Medical and Rescue Duties
First Responders should administer first aid
Others should dial 911 to report emergency and assist in directing first responders to scene

## Slide 25: Fire Prevention Plan
List of major fire hazards and handling, storage, and control procedures
Names of persons responsible for maintaining equipment and systems to prevent or control ignitions or fires
Name of persons responsible for controlling fuel source hazards
List of required training for all employees who have responsibilities in the plan
Evacuation procedures, including escape procedures and escape route assignments
Alarm systems
Fire hazards and prevention

## Slide 26: Fire Prevention Plan (Cont’d.)
Fire response procedures
Fire protection equipment
Critical plant operations shutdown procedure
Procedure to account for all personnel
Assignment of rescue and medical duties
Means for reporting emergencies
Identification of responsible persons to contact for further information

## Slide 27: Alarms
Yell for help
Main alarm system
Fire suppression system will automatically signal an alarm to the fire department
Notes: Question: What does your main alarm system consist of? Does it have a back-up alarm? Does it work if the electrical power is out?
Answers will vary.
Question: What is your company’s preferred means of reporting an emergency?
Answers will vary.

## Slide 28: General Plan Requirements
Available for employee review
Emergency training
Fire emergency alerts
Evacuation signals and alarm system
Evacuation routes and procedures
Employee accountability
Emergency response information

## Slide 29: Flammable and Combustible Liquids
Common materials people often use carelessly
Ignite with explosive force
Burn readily and give off twice the heat of an ordinary material fire
Notes: Question: Why should we be concerned about flammable and combustible liquids?
Answer: These materials ignite with explosive force and burn readily while giving off twice the heat of ordinary fires.

## Slide 30: Common Flammable and Combustible Liquids
Flammable liquids
  Isopropyl alcohol
  Propane
  Acetone, MEK, paint thinner
  Gasoline, kerosene
  Aerosol cans
Combustible liquids
  Oil
  Greases and lubricants
  Oil-based paints
Notes: Question: What other flammable or combustible materials do you use at work?
Answers will vary. Allow time for discussion.

## Slide 31: Flashpoint
Lowest temperature at which a liquid gives off enough vapors to be ignited
Low Flashpoint = High Flammability
Flammable liquids have a flashpoint less than 100˚F
Combustible liquids have a flashpoint greater than or equal to 100˚F
Notes: Questions: Consider the following scenario:
A driver has a portable gas tank (either plastic or metal) in the bed of his or her truck. While the driver was traveling to the gas station, the tank was free to move around in the truck bed. Because of this, the tank built up a static charge. When the driver stopped to put gas in the portable tank, s/he left the tank sitting in the truck bed instead of placing the container on the ground.
Invite students to discuss the possible consequences of the driver’s actions.
Answer: Since the driver did not remove the portable tank from the truck and place it on the ground, it was not “grounded.” Therefore, it is possible that when the gas nozzle touched the container the static discharged from the container and into the nozzle, which then ignited the gasoline fumes.

## Slide 32: Sources of Ignition
Lit cigarettes
Welding and cutting
Static electricity
Sparks
Hot equipment
Electrical equipment
Notes: Invite students to discuss their company’s smoking policy and designated smoking areas.
Question: Why do gasoline stations have “No Smoking” signs near the fuel pumps?
Answer: Because gasoline and its vapors are highly flammable. For that same reason, “No Smoking” signs are also placed near other flammable liquids and gases.

## Slide 33: Sparks and Heat Sources
Machinery and combustion engines
No flammables near hot work!
Ovens and heaters/blowers
Electric panels

## Slide 34: Risk Assessment/ SDS
Smoking restrictions
Proper storage
Proper dispensing
Fire and explosion data
Spill/leak response

## Slide 35: NFPA Label
Not as detailed as SDS
Flashpoint ratings in red square
4 = Below 73°F
3 = Below 100°F
2 = Below 200°F
1 = Above 200°F
0 = Will not burn

## Slide 36: NFPA Labeling

## Slide 37: Storage Room Requirements
Warning signs
Ventilated room
Explosion-proof electrical equipment
Covers over light fixtures

## Slide 38: Chemical Storage

## Slide 39: Indoor/Outdoor Storage Tips
Bonded and ground containers with flammables
Keep storage areas free of other combustible materials
Avoid stacking containers
Do not store with incompatible materials
Locate in a cool area, out of direct sunlight
Maintain safe distance from electrical panels or furnaces

## Slide 40: NFPA Labeling

## Slide 41: Safe Handling of Flammable Liquids
Static electricity is main concern
Spark-proof tools
Fire-resistant containers
Labeled containers
Use only what is needed
Practice good housekeeping
Welding/torch cutting restrictions

## Slide 42: Housekeeping Practices
Keep combustible dusts under control.
Dispose of contaminated rags.
Keep area free of combustible materials.
Keep exits clear.
Keep emergency response equipment access clear.
Notes: Question: What is your facility’s most serious housekeeping concern?
Answers will vary, but may include:
Combustible dusts such as sawdust, metal grindings, lint, or grain dust
Accumulation of cardboard boxes or wooden crates
Oily or solvent-soaked rags not disposed of properly

## Slide 43: Fire Hazards and Prevention
  Hazards and prevention:
    Cigarettes
      Generally prohibited
    Welding and cutting stations
      Maintain a clear 30 ft. radius
    Electricity
      Check for faulty wiring
    Hot equipment
      Keep free from rags or large dust build ups
    Combustible liquids or gases
      Store in cool, well-ventilated area
12
43/67
Notes: Talk about fire watch for welding

## Slide 44: Fire Response
Procedures
  Activate alarm.
  Set up equipment.
  Get a fire extinguisher.
  Evaluate the situation.

## Slide 45: Fire Response
General equipment requirements
  Fire extinguishers strategically located
  Manual foam or water systems
  Sprinkler systems
  Inspect firefighting equipment regularly
  Trained and authorized employees use equipment

## Slide 46: Extinguishing Agents
  Water
  CO2
  Dry Chemical
  Halon - used around electrical
AFFF - aqueous film fighting foam
APC - aqueous potassium carbonate

## Slide 47: Fire Basics
Class A – ordinary combustibles (wood, cloth, paper)
Class B – flammable liquids, gases, greases
Class C – energized electrical equipment
Class D – combustible metals
Class K – combustible cooking media (New)
A
B
C
D
Ordinary
Combustibles
Combustible
Metals
Flammable
Liquids
Electrical
Equipment
Notes: Question: How do you extinguish a class “B” fire?
Answer: Remove oxygen so vapors do not reach ignition source using foam, CO2, dry chemical or halon fire extinguishers.
Question: What are the characteristics of a class “C” fire?
Answer: White or black smoke coming from energized electrical equipment.
Question: What cautions should you take in extinguishing a class “K” fire?
Answers: Do not use water; evacuate unnecessary personnel.
Note: The class of extinguisher should be clearly marked on the extinguisher shell. The picture-symbol labeling system currently in use is designed to make the operation of fire extinguishers more effective and safe to use through the use of less confusing pictorial labels. The system also emphasizes when not to use an extinguisher on certain types of fires.

## Slide 48: Proper Fire Extinguishing Agents to Use on Different Classes of Fires
  Class A
    Cool the material below its flashpoint
    Use an ABC rated fire extinguisher
    Possible agents include pressurized water or foam
48/67

## Slide 49: Proper Fire Extinguishing Agents to Use on Different Classes of Fires (Cont’d.)
  Class B
    Water will make the fire worse!
    Eliminate the presence of oxygen
    Agents include foam, carbon dioxide, BC rated extinguishers, and halon
49/67

## Slide 50: Proper Fire Extinguishing Agents to Use on Different Classes of Fires (Cont’d.)
  Class C
    Water will not work!
    Use non-conductive agents
    Agents include carbon dioxide, BC rated extinguishers, and halon
50/67

## Slide 51: Proper Fire Extinguishing Agents to Use on Different Classes of Fires (Cont’d.)
  Class D
    Spread agents over the fire in a 1” thick blanket
    Agents include a sodium chloride base or special graphite base
51/67

## Slide 52: Proper Fire Extinguishing Agents to Use on Different Classes of Fires (Cont’d.)
  Class K
    Use dry chemicals
    Agents include halon, carbon dioxide, or foam
52/67

## Slide 53: Fire Suppression Equipment
Fixed fire extinguishing systems
Portable fire extinguishers

## Slide 54: Maintaining Portable Fire Extinguishers
Keep fully charged and in operable condition.
Keep in designated places at all times except during use.
Conduct annual maintenance checks.
Record the annual maintenance date and retain this record for one year.

## Slide 55: Portable Fire Extinguisher Training and Education
Employees must be provided with an educational program on:
  General principles of fire extinguisher use
  Hazards of incipient (beginning) stage fire- fighting
Employees designated to use extinguishers must receive instruction and hands-on practice in the operation of equipment

## Slide 56: Operating an Extinguisher
Pull the pin.
Aim at the base of the fire.
Squeeze the trigger.
Sweep side to side.
NOTE: Keep your back to an exit so you can escape if necessary
Notes: Display a fire extinguisher and allow students to hold it if they wish. Point out the location of the pin and simulate how to pull the trigger and sweep the area.
Invite students to share their experiences with using a fire extinguisher. Ask about the specific situation and how they and the people around them reacted to the situation.

## Slide 57: Firefighting Hazards
Flame
Heat
Smoke
Toxic vapors
Suffocation
Explosions

## Slide 58: First Aid Procedures
Get fresh air.
Flush the eyes.
Wash skin with soap and water.
If ingested, consult a doctor, and or activate EMS.

## Slide 59: Burn First Aid
Minor (first degree) skin burns are best treated with cool water
Second degree includes blistering
Third degree very deep and involve all layers of the skin

## Slide 60: Welding and Fire Safety
Obtain hot work permit.
Weld in designated area.
Inspect surrounding area for hazards (keep a 30 feet clear area around a cutting operation).
Post fire watch when needed and for the time required.

## Slide 61: Fire Safety Regulations/Codes
OSHA
  1910 Subpart E: Exit routes, emergency action/fire prevention plans
  1926.152: Flammable and combustible liquids
  1926.153: Liquefied petroleum gas
NFPA
  NFPA 30: Flammable and combustible liquids
  NFPA 51B: Fire prevention during welding, cutting and other hot work
  NFPA 55: Storage, use, and handling of compressed gases and cryogenic fluids in portable and stationary containers, cylinders, and tanks

## Slide 62: Chemical Hazards
May cause harm through inhalation or contact with the skin
Keep in a well-ventilated area
Can occur without heat
Symptoms
  Redness
  Irritation
  Burning
  Pain or numbness
  Blisters or dead skin
  Coughing or vomiting

## Slide 63: Chemical Spills
Evacuate the area.
Notify a supervisor or the emergency response team.
Remove ignition sources (if safe to do so).

## Slide 64: Diked Spills
Before draining a diked area of rainwater. Check to make sure there is not a visible sheen of oil on the surface.

## Slide 65: Natural Gas
In any form, a minute amount of odorant such as t-butyl mercaptan, with a rotting-cabbage-like smell, is added to the otherwise colorless and almost odorless gas, so that leaks can be detected before a fire or explosion occurs. Sometimes a related compound, thiophane is used, with a rotten-egg smell.
Adding odorant to natural gas began in the United States after the 1937 New London School explosion. The buildup of gas in the school went unnoticed, killing three hundred students and faculty when it ignited. Odorants are considered non-toxic in the extremely low concentrations occurring in natural gas delivered to the end user.

## Slide 66: Training Reminder
Training on relevant emergency procedures and first aid
For new hires – within 30 days
Refresher Training – once per year

## Slide 67: Summary
Understand how to prevent emergencies.
Understand emergency response.
Only use fire-fighting equipment if trained.
Know your role in an evacuation.
Apply this information at work and at home.
Ask your supervisor.