## Slide 1: Domain 1: Safety Awareness
Section 5:
Personal Protective Equipment (PPE) and Programs
CFR Part 1910 Subpart I (§1910.132 to 1910.138)
Foundations of
Manufacturing
Notes: Read Lesson Link aloud to students:
In this module, we will discuss how to select the proper personal protective equipment (PPE), each component of the PPE, the function of these components, their use, and how and when to wear these components. We will also discuss information on hearing, sight, and respiratory protection. Remember, safety is the company’s primary concern. An employee who knows the proper use and wear of PPE can save lives and reduce injury and illness of employees, thereby reducing medical cost, lost time, and even unemployment and workers’ compensation costs. Additionally, employers are required to establish a program to protect their respirator-wearing employees from injuries that can result in lost time and adverse long-term health hazards. Currently, over five million respirator wearers work in an estimated 1.3 million general industry, construction, shipyard, longshoring and marine terminal workplaces. Respiratory protection training is essential to meeting this goal.

## Slide 2: Learning Objectives
Describe how to conduct a hazard assessment inspection.
Identify proper selection of necessary PPE for hazards.
Describe function, use, and maintenance of PPE and respirators.

## Slide 3: Learning Objectives (Cont'd.)
Examine OSHA Requirements for Respiratory Protection, hazards associated with the use of respirator protection, and company program requirements for respirator safety.
Identify types of respirators.
Demonstrate the proper method for placement and removal (donning and doffing), ensuring proper fit, cleaning, maintenance, and storage of respirators.

## Slide 4: Hazard Assessment
Evaluate every job function available
Determine
  If hazards are present
  PPE requirements
Notes: Question: Why would an employer assess hazards to determine if PPE is warranted?
Answers will vary, but should include: “To ensure that employees are as safe as possible in all situations.”

## Slide 5: Eye and Face Hazards
Flying particles
Molten metal
Liquid chemicals
Vapors or gases
Acids and caustic liquids
Light radiation injuries
Notes: Question: Why should an employer have adequate PPE available?
Answers will vary, but should include:
To prevent injury to personnel and equipment
To meet OSHA standards
Invite students to discuss potential eye and face hazards specific to their jobs.

## Slide 6: Head Hazards
Falling objects
Exposed electrical conductors
Low-hanging obstructions
Notes: Question: What type of head protection would you wear around exposed electrical conductors?
Answer: Non-metal
Invite students to discuss potential head hazards specific to their jobs.

## Slide 7: Foot Hazards
Falling or rolling objects
Objects piercing the sole
Slippery surface
Hazardous chemicals
Extreme weather conditions - cold
Notes: Invite students to discuss potential foot hazards specific to their jobs.

## Slide 8: Hand Hazards
Skin absorption
Cuts or lacerations
Abrasions
Punctures
Chemical and thermal burns
Notes: Invite students to discuss other potential hand hazards specific to their jobs.

## Slide 9: Assessment Documentation
Identifies:
Workplace
Department
Area or job function evaluated
Person or persons who conducted and certified assessment
Completion date
Type of PPE selected

## Slide 10: Clothing
Fire resistant (welding)
Leather or rubber gloves, aprons, and shoes (heavy, sharp, or rough materials)
Close fitting (moving machinery)
Heat/Cold resistant (hot or cold object or materials)
Chemical resistant

## Slide 11: Employee Training
Know when PPE is necessary.
Demonstrate proper use of PPE.
Determine type of necessary PPE.
Know limitations of PPE.
Know how to don/doff, adjust, and wear PPE.
Properly care for, store, and inspect PPE.

## Slide 12: Employee Training (Cont'd.)
Retraining is required when:
Workplace changes require new PPE
PPE changes (upgrades)
Documented improper use or wear of PPE by one or more employees

## Slide 13: Eye and Face Protection
Must meet ANSI Z87.1-1989 standards
Safety glasses
  Flying objects
Goggles
  Dust
  Liquid materials
  Gases and vapors

## Slide 14: Eye and Face Protection (Cont'd.)
Face shield
  Overall protection for the face and eyes (does not eliminate need for safety glasses)
Shaded filter lenses
  Protects the eyes from bright welding arc or flame
Prescription eyewear
  Use polycarbonate lenses, no glass or contact lenses
  Use side shields
Notes: Note: Face shields are often worn as additional protection over goggles or safety glasses, but they should not be worn as the primary eye protection.

## Slide 15: Wear and Care of Eye Protection
Fits comfortably
Vision not blocked or distorted
Use before exposed to the hazards
Clean up with soap and water
Dispose of scratched or damaged glasses

## Slide 16: Noise
Noise induced hearing loss is caused by sound power levels greater than 85 decibels average over an 8 hour period
Affects the ability to hear high frequency sounds

## Slide 17
Types of Hearing Loss
Conductive
Sensorineural
Mixed

## Slide 18: Types of Hearing Protection
Reduce intensity of sound
Ear plugs
Ear muffs
Ear plugs and ear muffs combined
Cotton in ears not effective
Noise level testing is regulated by the Environmental Protection Agency (EPA)

## Slide 19: Hard Hats
Meet ANSI Standard Z89.1-1997
High density polyethylene
Non-conductive

## Slide 20: Classes of Hard Hats
Class A (now G)
General service (e.g., mining, building construction, shipbuilding, lumbering, and manufacturing)
Good impact protection but limited voltage protection
Class B (now E)
Electrical work
Protect against falling objects and high-voltage shock and burns
Class C (still C)
Designed for comfort, offer limited protection
Protect heads that may bump against fixed objects, but do not protect against falling objects or electrical shock
Notes: If possible, provide samples of head protection.

## Slide 21: Hard Hat Wear and Care
Fit comfortably
Webbing and strapping act as shock absorber
Do not wear or put anything under hard hat
Wash with soap and water only
Inspect for damage before each use
Hard hats are not step stools

## Slide 22: Foot Protection
Steel-toed boots
Metatarsal and ankle protection
Puncture or slip-resistant soles
Chemical resistance
Waterproof boots
Cold weather foot wear
Notes: If possible, provide samples of foot protection. Clarify between steel toe and other types of safety shoes.

## Slide 23: Wear and Care of Foot Protection
Footwear should be comfortable
Inspect boots before each use
No cracks or holes in chemical or waterproof boots
Soles checked for excessive wear
Keep clean and dry

## Slide 24: What are some of the hand injuries you need to guard against?
Burns
Bruises
Cuts
Abrasions
QUESTION
Punctures
Fractures
Amputations
Chemical Exposures

## Slide 25: Hand Protection
Chemical-resistant gloves
Kevlar, metal mesh, cut-resistant gloves
Leather work gloves
Specialty gloves

## Slide 26: Wear and Care of Hand Protection
Comfortable fit
Inspect gloves before each use
Keep clean, dry and oil free
Regularly check electrical gloves
Discard if damaged or contaminated

## Slide 27: General Work Clothing Guidance
Long sleeves and pants
Cold weather gear
Flame-retardant
No loose clothing and jewelry
Chemical-resistant clothing

## Slide 28: What’s wrong with this picture?
Notes: No safety glasses
No hearing protection
No heavy work gloves
No Brains!!!

## Slide 29: Welding PPE
Welding Gloves (leather)
Welding Helmet (does not replace need for safety glasses with side shields)
Leather Apron

## Slide 30: Hot Work Permits
Any process that creates sparks or involves heat or open flame is considered HOT WORK
  Riveting
  Welding, cutting, burning, heating
OSHA recommends work be done in special area
If not possible combustible materials are required to be at least 35 feet away from source of hot work

## Slide 31: Confined Spaces CFR 1910.146
Confined Spaces – storage tanks, ventilation ducts, and pits more than four feet deep are considered confined spaces.
  Dangerous atmosphere
  Material that could potentially drown
  Structure that could trap or suffocate
  Any other recognized serious safety or health hazard

## Slide 32: Confined Spaces CFR 1910.146
EXAMPLES OF CONFINED SPACES
Underground utility vaults
Storage tanks
Process vessels
Storage bins
Silos
Boilers
Ventilation or exhaust ducts
Sewers
Tunnels and pipelines
Manholes
Open top spaces more than 4 feet in depth (pits, deep holes)

## Slide 33: “Permit Required Confined Spaces”
May contain a hazardous atmosphere
Contains material that has the potential to engulf an entrant
Has walls that converge inward or floors that slope downward that could trap or asphyxiate an entrant
Contains any other recognized safety or health hazard

## Slide 34
“Permit required confined spaces” must be identified by the employer
Employees who may have to enter “Permit required confined spaces” must be informed of their existence and location and their hazards
Must provide additional training to all employees who may have to enter a “permit required confined space”
Only those who have completed the relevant training and hold a permit are allowed to enter and/or work in a “permit required confined space”
The employer must have a system in place for issuing permits
Access to a confined space should be restricted
“Permit Required Confined Spaces” (Cont’d.)

## Slide 35: Respiratory Protection
Filtering facepiece
Air-purifying respirators
Air-supplied respirators
SCBA
NIOSH

## Slide 36: Respiratory Protection (Cont'd.)
Employee Responsibilities
Medically approved respirators
Fit test annually
Inspect before use
Seal check
Notes: Question: When would an employee use respiratory protection?
Answers will vary, but may include:
During a chemical spill
When painting, sanding, drilling
When fumes are present in the workplace
During a fire
In a dust-filled room

## Slide 37
General Respiratory Program Requirements
Establish a written program.
Conduct regular program evaluations.
Address air quality standards.
Conduct medical examinations.
Conduct respirator training and fit testing.
Ensure proper selection of respiratory equipment.
Control hazards, using respirators as a last resort.
Address inspection, cleaning, maintenance and storage.
Employer Responsibilities

## Slide 38
Respiratory Protection Training Requirements
Training conducted prior to job assignment
Discuss equipment operation, capabilities, and limitations
Why respiratory protection is required
Why a particular respirator has been selected
Proper maintenance and storage of respirators
Inspection, donning, fit checks and proper wear
Nature, extent and effects of respiratory hazards

## Slide 39: Respiratory Protection Retraining Requirements
Near-miss event – (accident without injury)
Respiratory injury
Change in job assignment
New hazards or equipment
New hazard control methods
Failure in the safety procedures
Reason to doubt employee proficiency
Respiratory
Protection
Retraining
Notes: Question: Why should employees be retrained when they change job assignments?
Answers will vary, but may include:
Job assignment may require the use of different equipment,
Hazards may be different in the new assignment, and/or
Risks may be different in the new assignment.

## Slide 40: Respiratory Protection Program Development
Establish program administrator.
Establish policy/SOPs.
Conduct hazard analysis of the facility.
Determine respiratory hazard control measures.
Eliminate respiratory hazards where possible.

## Slide 41: Respiratory Protection Program Development (Cont'd.)
Conduct training (initial and refresher).
Provide protection where hazard elimination is not possible.
Perform inspections and maintenance.
Periodically audit the program.
Modify policies/SOPs.

## Slide 42
Purpose of a Respiratory Protection Program
Primary goal is to reduce or eliminate respiratory hazards by:
  Eliminating hazard-producing equipment
  Implementing administrative controls
  Implementing engineering controls
  Issuing respiratory equipment
  Providing training and procedures

## Slide 43
Respiratory Basics
Alveoli
Notes: Question: What are alveoli?
Answer: Cells in the lungs that transmit oxygen to the blood and transmit wastes to the lung for exhalation.

## Slide 44
Types of Respiratory Hazards
Gases
  Generally used in a compressed form
  Can be released by chemical processes or high heat
  Can affect all routes of entry
Vapors
  Formed by evaporation of liquids or solids
  Amount usually depends upon exposed surface area
  Can be deadly

## Slide 45
Types of Respiratory Hazards (Cont'd.)
Fumes
  Metallic and formed by welding, cutting, or brazing operations
  Extremely hazardous to inhale
Air particulates
  Composed of solid or liquid particles that are suspended or dispersed in air
  Can be explosive and hazardous to breathe

## Slide 46
Types of Respiratory Hazards (Cont'd.)
Atmospheric Hazards
  Serious risk to employees from one or more of the following causes:
  Flammable gas, vapor, or mist exceeding 10% LEL
  Airborne combustible dust in excess of its LEL
  Oxygen concentration below 19.5%
  Oxygen concentration above 23.5%
  Concentration of any substance exceeding its PEL
  Another atmospheric condition is IDLH
Notes: Question: What is the normal oxygen concentration – by volume – in the air?
Answer: 21%
Note: An IDHL level poses an immediate threat to life, causes irreversible adverse health effects, or impairs an individual's ability to escape from a dangerous area.

## Slide 47: Exposure Limits
Permissible Exposure Limit (OSHA):
  Permissible exposure limits (PELs)
  29 CFR 1910.1000 establishes OSHA’s exposure levels
Recommended Exposure Limits (NIOSH):
  Recommended exposure limits (RELs) used to develop new OSHA standards
  “NIOSH Recommendations For Occupational Health Standards”

## Slide 48
TLV is the upper limit of a toxic concentration to which you can be exposed without adverse effects.
Gaseous substances: parts per million (ppm)
Fumes or mists - milligrams per cubic meter (mg/m3)
American Conference of Governmental Industrial Hygienists (ACGIH)
Threshold Limit Value

## Slide 49
Maximum concentration of a toxic substance
Determining use and type of SCBA
Immediately Dangerous to Life and Health (IDLH)

## Slide 50
Medical Requirements
Cleared by a physician
Understanding respirator criteria

## Slide 51: Particulate Respirators
  Only protect against particles like dust
  Do not protect against chemicals, gases, or vapors
  Air purifying respirators
51/77

## Slide 52: Filter Basics
Filters are rated in microns. The larger micron number, the larger the particles can pass thru it.
The absolute rating, of cut-off point, of a filter refers to the diameter of the largest spherical glass particle, normally expressed in micrometers (mm), which will pass through the filter under laboratory conditions.
Items shown are filter elements

## Slide 53
Types of Respirators
Air-purifying
Supplied-air
Self-contained breathing apparatus

## Slide 54
Types of Respirators (Cont'd.)
Air-Purifying
Does Not Produce Oxygen
Used where there is enough oxygen present, but the air in the area is contaminated with gases, vapors, or dust
Filter out dangerous materials or divert air through a chemical filter
WARNING: Some substances cannot be safely filtered, which requires the use of an air-supplied respirator

## Slide 55
Types of Respirators (Cont'd.)
Air-Purifying: Mechanical-Filter
Remove particles from the air
May have disposable filters for dust
May have half-face or full-face face pieces
To choose the correct unit you need to know:
- Type of contaminant
- Concentration of the contaminant
- Size of the particles

## Slide 56: Types of Respirators (Cont'd.)
Used for low concentrations of:
  Organic gases
  Pesticides
  Paint vapors
May have half-face or full-face face pieces
Cartridge must be correct for the type of contaminant
Use only with contaminants with warning odor or irritation
Not for use against highly toxic gases
Air-purifying: Chemical Cartridge
Notes: WARNING - Some substances cannot be safely filtered. In those cases, you are required to wear an air-supplied respirator.

## Slide 57: Types of Respirators (Cont'd.)
Protects against certain gases and particles
Battery powered motor draws air through a filter
Air-purifying: Gas-Mask Type
Protects against certain gases and particles
Most have full face piece
Most use chin-mount canisters
Powered air-purifying: Hooded Type

## Slide 58
Used when not enough oxygen or concentration of airborne substances is IDLH
Approved for each contaminant
Types Of Respirators (Cont'd.)
Supplied-air Respirators

## Slide 59
Self-contained Breathing Apparatus (SCBA)
  Breathable source of air for limited duration
  SCBA consists of the following:
  Face piece
  Breathing tube
  Air supply tube
  Regulator
  Exhalation valve
  Air cylinder and valve
Types of Respirators (Cont'd.)
Notes: Question: Who would normally use an SCBA?
Answer: Trained rescue personnel

## Slide 60
Types of Respirators (Cont'd.)
SCBA
Mobile Air Supply Type Systems
Closed-circuit rebreathing units
Pressure-demand open circuit units

## Slide 61
Types of Respirators (Cont'd.)
SCBA
Closed-Circuit Rebreathing Units
Protects up to four hours
Typically used in mine rescues
User’s breath is recycled
Carbon dioxide removed from exhaled air
Oxygen added from a small cylinder

## Slide 62
Types of Respirators (Cont'd.)
SCBA
Pressure-demand Open-circuit Units
Provides 30 to 60 minutes of air
Typically used by fire rescue services
The user’s breath exhaled into atmosphere
Positive pressure maintained inside the face piece

## Slide 63
Respirator Components
Head Harness
Facepiece
Eyepiece
Oral/nasal cup
Inhalation valve
Inhalation valve seat
Air-purifying Element
Exhalation Valve Seat
Exhalation Valve
Exhalation Valve Cover
Notes: Question: What components of the respirator should be inspected to ensure that they are working properly?
Answer:
Inhalation valves
Exhalation valve
Head straps
Facepiece

## Slide 64: Inspection Before Use
Employees must inspect their own equipment prior to use.
Remove components from service if function is adversely affected.

## Slide 65
Develop detailed inspection policy.
Document each inspection.
Inspect all components before use.
Tag unusable, damaged equipment.
Inspection Considerations
INSPECTION
CHECKLIST
FOR
RESPIRATORS

## Slide 66: Inspection Considerations (Cont'd.)
Inspect equipment before each use.
Consider the effects on equipment stored for long periods.
Remove contaminated equipment from service immediately.
Incorporate manufacturer’s instructions into plant inspections.

## Slide 67: Fit and Seal Testing
Prior to use the individual must know how:
  to put on and take off a respirator,
  it should be positioned on your face (nose, chin, and cheek position),
  to adjust strap tension, and
  to tell if the respirator fit is comfortable.
Notes: Note: Instructor demonstration is required.
Question: How often should your respirator be fit-tested?
Answer: Once every calendar year.
Question: Why every year instead of 3 to 5 years?
Answer: People lose or gain weight; their faces may change from the weight difference. Medical conditions change from year to year. Accidents may change the sealing surface of the face.

## Slide 68
Performed prior to every use
Steps to follow determined by:
  OSHA’s required positive and negative pressure checks, or
  Respirator manufacturer's recommended user seal check method shall be used
Not a substitute for qualitative or quantitative fit tests
Seal Check Requirements

## Slide 69
Seal Check Requirements (Cont'd.)
Positive Pressure Check (Exhaling)
Close off the exhalation valve and exhale gently into the facepiece.
Face fit is satisfactory if a slight positive pressure can be built up inside the facepiece without evidence of outward leakage at the seal.
Cover
Exhalation Valve
Notes: Note: Instructor will demonstrate each step of the seal check procedures.

## Slide 70
Seal Check Requirements (Cont'd.)
Negative Pressure Check (Inhaling)
Close off the inlet opening of the canister or cartridge(s) by covering with the palm of the hand(s) or by replacing the filter seal(s).
Inhale gently so that the facepiece collapses.
Hold breath for ten seconds.
Notes: Note: Some cartridge inlet designs cannot be effectively covered with the palm of the hand. In this case, try covering the inlet with a thin latex or nitrile glove to check the seal. If the facepiece remains collapsed with no inward leakage of air, the air-tightness is considered satisfactory.
Note: The respirator manufacturer's recommended procedures for performing a user seal check may be used instead of the positive and/or negative pressure check procedures provided that the employer demonstrates that the manufacturer's procedures are equally effective.

## Slide 71: Qualitative Fit Testing
Also known as “The Gas Chamber” test
Follow OSHA’s mandatory procedures
Test required upon issue of respiratory equipment
Irritant smoke or banana oil can be used
Participants must recite a standard phrase before being released from the testing area
Notes: Question: What is qualitative fit testing?
Answer: A pass/fail fit test to assess the adequacy of respirator fit that relies on the individual's response to the test agent.

## Slide 72: Quantitative Fit Testing
Follow OSHA’s mandatory procedures
Numerically measuring the amount of leakage into the respirator
Measures concentration of irritant inside the mask using instrumentation and personnel responses
Notes: Question: What is quantitative fit testing?
Answer: An assessment of the adequacy of respirator fit by numerically measuring the amount of leakage into the respirator.

## Slide 73: Final Fit Test Considerations
Normal breathing
Deep breathing
Turning head from side to side
Talking
Bending
Jogging in place

## Slide 74: Cleaning and Disinfecting Considerations
Read the manufacturer’s guidelines first.
Disassemble according to procedures.
Scrub respirators in detergent and warm water.
Treat with disinfectant.
Re-rinse to remove detergent and disinfectant.
Air-dry, do not dry rubber under heat or sunlight.
Never use solvent to clean plastic or rubber.
For SAR and SCBA units consult the manufacturer’s guidelines for cleaning and disinfecting procedures.
Notes: Question: Why are some solvents not appropriate to use when cleaning a respirator?
Answer: Solvents can deteriorate the rubber, causing it to be ineffective when stretched over head or making a seal to the face.

## Slide 75: Storage Considerations
Protect from sunlight, heat, cold, moisture and chemicals.
Place respirators in individual sealable plastic bags.
Emergency-use units should be stored according to manufacturer’s guidelines.
For SAR and SCBA units consult the manufacturer’s guidelines for storage.

## Slide 76: Fit Test Demonstration
Inspect the unit for damage.
Put the respirator on (using steps to ensure proper fit).
Test the unit to ensure a proper seal.
Conduct six exercises while wearing unit.
Properly take off the respirator.
Clean the respirator.
Store the respirator.
Notes: Respiratory Protection Equipment Fit Test Exercise 1-5-1
Introduction: The purpose of this exercise is to instruct students on the proper procedures for inspecting, donning, doffing and fit-testing a respirator.
Distribute the handout for Exercise 2-4-1 and one respirator per team.
Guide students through inspecting and donning the respirator.
Assist students in following fit test/breathing steps.
Inform students that when performing the talking portion of step four the subject shall talk slowly and loudly enough so the test conductor can hear him clearly. The subject can read from a prepared text such as the Rainbow Passage below, count backward from 100, or recite a memorized poem or song.
Rainbow Passage:
“When the sunlight strikes raindrops in the air, they act like a prism and form a rainbow. The rainbow is a division of white light into many beautiful colors. These take the shape of a long round arch, with its path high above, and its two ends apparently beyond the horizon. There is, according to legend, a boiling pot of gold at one end. People look, but no one ever finds it. When a man looks for something beyond reach, his friends say he is looking for the pot of gold at the end of the rainbow.”
Assist students to ensure that the respirator is properly removed, cleaned and prepared for storage.
Discuss student concerns and questions.

## Slide 77: Summary
Job safety is employer’s number one priority
Assessing hazards is essential
PPE selection, use, and care
Respiratory protection program elements:
  Evaluations
  Fit testing
  Hazard analysis
  Training