## Slide 1: Domain 2: Production and Processes
Foundations of Manufacturing
Section 3: Manufacturing Essentials and Instruments
Notes: Read Lesson Link aloud to the students:
In order to be an effective production technician, you must have a working knowledge of what work orders, blueprints, and paper or computer controls you will likely encounter in any of the 14 manufacturing sub-industries. In this module, you will learn the basics of these elements that span the sub-industries.

## Slide 2: Learning Objectives
Identify manufacturing instruments.
Describe use of instruments.
Discuss control of instruments.
Examine various hand-held tools and gauges.
Notes: Direct students to turn to page 2-3-1 in their Foundations of Manufacturing, Domain 2: Production and Processes, Section 3: Manufacturing Instruments, Student Workbook and continue with the discussion.

## Slide 3
Learning Objectives (Cont’d.)
Repairs and adjustments are made to production equipment
Set-up meets process requirements and specifications
First piece or production run meets specifications
Set-up procedures are documented for repeatability
Set-up meets ergonomic, health, safety, and environ- mental standards
Set-up meets equipment specifications
3/88

## Slide 4: QUESTION
What are the most important skills necessary to do your job?
  Knowing how to use the tools required
  Understanding the equipment involved
  Communicating with others
  Teamwork

## Slide 5: Skills Essential for Manufacturing
Understand manufacturing processes
QA procedures
Read technical prints and drawings, specifications
Equipment maintenance
Documentation procedures

## Slide 6: Operating Instruction Sheets
Contain tool and equipment requirements for particular part numbers
Don’t substitute without permission from proper authority

## Slide 7: Bill of Material (BOM)
Engineering: reflects product as designed by engineering; ECN’s note change to design
Manufacturing: reflects product as planned by manufacturing, listing parts, materials, and tools
7/88

## Slide 8: Bill of Material Example
14
8/88

## Slide 9: BOM Sub-Parts
16
9/88

## Slide 10: BOM Showing Parts and Sub-Parts
17
Part level numbers reflect assemblies and sub assemblies
10/88

## Slide 11: Identification, Use, and Control of Instruments
Control – on/off and automatic process
Process variables – pressure, temperature, flow
Control signals – transmit information
Units of measurements – PSI, temperature (C & F), GPM, etc.
Gauges – display pressure, temperature, flow, etc.
Open and closed-loop control systems
Notes: Question: In your plant, what is the most common system that is controlled automatically?
Answers will vary.

## Slide 12: Process Control
Typical Process Measurements
  Temperature
  Pressure
  Flow
  Level
Condition Monitoring
  Humidity
  pH
  Vibration
  Speed/RPM

## Slide 13: Temperature
Four scales
  Fahrenheit: water freeze 32 °, boils 212°
  Celsius (Centigrade):water freeze 0 ° and boils 100°
  Kelvin: water freeze 273 ° and boils 373 °
  Rankine: water freeze 492 ° and boils 672 °

## Slide 14: Temperature Scales

## Slide 15: Conversions
°F = (1.8) (° C)+32
  If ° C=20, °F=68
°C = (°F-32)/1.8
  If °F=86, °C=30

## Slide 16: Conversions
Lbs x .454 = Kilogram (1Kg = 2.2 lbs)
Miles x 1609 = Meters
32 degrees Fahrenheit = 0 degrees Celsius
1 inch = 2.54 cm or 25.4 mm
1 meter = 39.37 inches

## Slide 17: Temperature Measurement Devices
Thermometer

## Slide 18: Level Measurement Devices
Two types
  Direct
    Dipstick
    Sight Glass
    Float
    Displacers
  Indirect
    Pressure (hydrostatic head)
    Bubbler
    Magnetic
    Conductance
    Capacitance
    Other – Ultrasonic, radar

## Slide 19: Dipstick

## Slide 20: Sight Glass

## Slide 21: Units of Pressure
PSIA – Pounds per square inch absolute
PSIG – Pounds per square inch gauge
Inches of water or mercury
Psia = psig + atmospheric

## Slide 22: Units of Pressure (Cont’d.)
Atmospheric = 14.7 psi at sea level (the weight of a column of air from the ground to the upper atmosphere)
0 psig = 14.7 psia
1 bar = 1atm
1 Pascal = .000145 lb/sq-in

## Slide 23: Pressure Conversions
A pressure gauge that measures psig indicates a reading of 50. The local atmospheric pressure is 14.7 psi. What is the absolute pressure (psia) that corresponds to the psig reading?
Example 1
Notes: ANSWER- 50+14.7=64.7

## Slide 24: Pressure Conversions (Cont’d.)
A psia pressure-measuring instrument indicates a
reading of 42.5 psia. The local atmospheric pressure is 14.6 psi. What is the corresponding gauge pressure (psig)?
Example 2
Notes: 42.5-14.6=27.9

## Slide 25: Pressure Conversions (Cont’d.)

## Slide 26: Pressure Measurement Devices
Manometers – A column of liquid will seek a certain height based on the pressure exerted on the liquid

## Slide 27: Flow
Flow is the quantity of fluid that passes a given point per unit of time.
3 Types
  Laminar: smooth flow
  Turbulent: erratic flow
  Transitional: mixed
Pressure is exerted in two directions
  In the direction of flow
  On the walls of the pipe

## Slide 28
Magnetic Flow Meter
28/88

## Slide 29: Example of Flow Meter

## Slide 30: Examples of Gauges

## Slide 31: Dual Scale
1000 kPa = 145 psi, 6000 kPa = 870 psi

## Slide 32: 3-Scale Gauge

## Slide 33: Numbers
Represent items in quantity
Originally digitus (Latin), meaning finger or toe

## Slide 34: Decimals
decem- ten (10)
Hindu-Arabic numbers (0 – 9)
Digits in groups of 3
465,234,895,159.000
billions millions thousands hundreds fractions
1 5 9 . 0 0 0
hundreds tens ones zero tenths hundredths thousandths

## Slide 35: Decimal Fractions

## Slide 36: Rounding Off

## Slide 37: Adding/Subtracting Decimals
Like addition or subtraction on columned numbers- place value rules
2.24
3.119
6.0412
Ans. 11.4002
12.19
5.42
Ans. 6.77

## Slide 38: Multiplying Decimals
Same as multiplying numbers
Add up total decimal places
3.22 (two)
x 2.7 (one)
______
2254
6440
______
Ans. 8.694 (three decimal points)

## Slide 39: Dividing Decimals
Divisor- number you are dividing BY
Eliminate decimal by moving to the right
Done by multiplying by 100
Must do multiplication to BOTH numbers (divisor and dividend)
Carry decimal point up to top line (answer)
Times 100 moves decimal 2 places to right

## Slide 40: Various Hand-held Tools and Gauges
Calipers – measure distance between two opposing sides
Micrometers – precisely measure thickness of blocks, outer and inner diameters and depths. Ten time more accurate than calipers.
Multimeters – electrical measuring instruments that measure more than a single quantity

## Slide 41
Inside and Outside Calipers
41/88

## Slide 42: Examples of Calipers

## Slide 43: Example of Vernier Caliper

## Slide 44: Vernier Caliper

## Slide 45
Dial Caliper
45/88
Notes: The dial caliper on wisc on line

## Slide 46: Example of Digital Caliper

## Slide 47: Micrometers
External
Internal
Depth
Notes: Question: Have any of you ever seen a micrometer? If so, what type was it?
Answer will vary.

## Slide 48: Parts of a Micrometer

## Slide 49: Use of a Micrometer

## Slide 50: Example of Depth Micrometer

## Slide 51: Use of Depth Micrometer
Notes: Depth Micrometer review on wisc on line

## Slide 52
Pocket Multimeter from the 1920s
52/88

## Slide 53
Analog Multimeter
53/88

## Slide 54
Digital Multimeter
54/88

## Slide 55: Multimeters
Analog
Digital
Notes: Questions: How many of you have used the tools and gauges listed? Which ones?
Have you used others not mentioned? Which ones?
Answers will vary.

## Slide 56
Differential Pressure Transmitter
56/88

## Slide 57
Measuring Temperature
57/88
Notes: Differential Pressure Transmitters measure the difference in pressure between two ports. They are used to measure level in a tank and flow through an orifice plate.

## Slide 58
Level Float Switch
58/88

## Slide 59
Instruments Used to Measure Process Variables
PRESSURE
Differential pressure transmitters
TEMPERATURE
Thermocouples
Resistance temperature deterctors (RTDs)
FLOW RATE
Instruments that measure mass
Differential pressure instruments
LIQUID LEVELS
Level floats (direct measurement)
Pressure transmitters (inferential measurement)
Magnetic flow meters
Pressure transducers
Thermistors
59/88

## Slide 60
Choosing an Instrument to Measure Pressure
Type of Measurement
Gauge pressure
Process Condition
Pressure
Process Fluid and its Properties
Clean
Absolute pressure
Temperature
Line Size
Flow
Dirty
Solids in Suspension
Gas
Liquid
Condensable vapor
Jellies
Freezes
60/88

## Slide 61
Thermocouple Assembly
61/88

## Slide 62
Different Types of Flow Measurement Instrumentation
62/88

## Slide 63
Functionality of Floats Versus Differential Pressure Transmitters
63/88

## Slide 64
Open Loop System versus Closed Loop System
Open Loop Controller Unit
Driver
Motor
Driver
Motor
Feedback Control
Closed Loop Controller Unit
64/88

## Slide 65
Controlling Instruments
65/88

## Slide 66
HART Protocol
66/88
Notes: Highway Addressable Remote Transducer (HART)

## Slide 67
How HART Works: Digital over Analog
67/88

## Slide 68
Engineering Tolerances
Engineering Tolerances
physical dimension
measured value
spacing
physical property
68/88

## Slide 69
Status of First Production Run
Design and specification
Set-up to meet specs
First production run
Inspection of first piece
Document for repetition
Production can go ahead
69/88

## Slide 70
Instrument Calibration
70/88

## Slide 71
Specifications
Validation gives an assurance that products meet the needs of customers and any other stakeholders that have been identified
Verification is a formal evaluation that decides whether it meets the standards and specifications required
Frequently responsibility of operator to confirm gauges are current in calibration prior to using
71/88

## Slide 72: Overview of Instrument Maintenance and Repair

## Slide 73: Instrument Inspection
Inspections lead to one of the following outcomes:
  No Action
  Adjustment
  Repair
  Replace
Notes: Thorough inspections are the basis for appropriate instrument maintenance, leading to one of the following outcomes:
  No maintenance activity required
  Adjust
  Repair
  Replace
Although they vary widely in cost, instruments are expensive to replace.
Therefore, instruments must be maintained

## Slide 74: Instrument Inspection
Inspections should occur at regular intervals based on:
  Intensity of use
  Criticality of accurate output to reliable process monitoring
Notes: Frequency of Instrument Inspections
Although an instrument maintenance schedule may begin, basing the inspection frequency on make and model number, over time, the schedule will need to be adjusted so that similar instruments are inspected, based on:
Intensity of use.
  Criticality of accurate output to reliable process monitoring.

## Slide 75: Working in Hazardous Zones
Instruments in hazardous zones should not be repaired there.
  Confined spaces
  Intrinsically safe zones
Problem instrument should be moved to a safe zone for repair.

## Slide 76: Overview of Instrument Adjustments
Sensor Orientation
Configuration Setting
Span
Sample Rate
Noise Filters
Notes: A wide variety of Adjustments may be required over the life of the instrument, but they are all intended to increase the process-specific accuracy of the data being reported from the instrument to the control system.
An adjustment is not considered to be a repair, but many adjustments require the instrument to be isolated or taken out of service.

## Slide 77: Ideal Accuracy Peak
Notes: Ideally, the instrument’s peak accuracy will exceed the process range.

## Slide 78: Overview of Instrument Replacement
Remove old failing unit
Install new or refurbished unit
Commission (recommission)
Notes: From time to time, instruments will need to be replaced.
The old, failing unit will be discarded, or sent to the shop for an onside repair, or possibly sent for outside service.
A new or refurbished instrument will be installed in its place.
If a new unit it will be installed, it must be commissioned.
If a unit is repaired and returned to service, it must be recommissioned.

## Slide 79: Instrument Return to Service
Verify function
Confirm calibration
Check trip function
Confirm loop communications
Notes: The objective of instrument return to service is to make sure the repaired unit is ready for operation.
  Does the sensor have output?
  Is it accurate?
  Will it trigger alarms/stop of the operation?

## Slide 80: Calibration
Functioning
Accurate
Emergency Shut-down (ESD) works
Calibration - Instruments that measure PV (process variables) need to be checked to make sure:
(Continued)

## Slide 81: TOOL CALIBRATION
Calibration is defined as “adjusting a tool to a standard”.
Used to ensure continued accuracy of the measurement device.
Documented on tool.
Intervals determined by company standards based on reliability needs
DUE DATE is most important

## Slide 82: Calibration (Cont’d.)
Purpose of calibration is to make sure that the instrument produces an accurate output across the measured range.
Usually the standard is 4X more accurate than the desired instrument accuracy.

## Slide 83: Calibration (Cont’d.)
Probe replacement
Range or span of measurement
Component aging
Zero base changes
Process corrosion
Calibration changes: Things that may affect calibration include:

## Slide 84: Rejected Calibration

## Slide 85: Micrometer Calibration
Gage blocks used to calibrate a micrometer

## Slide 86: Gauge Blocks

## Slide 87: Summary
Identification of instruments
Use of instruments
Control of instruments
Various hand-held tools and gauges

## Slide 88
Any Questions
How do we identify manufacturing instruments?
How do we describe the uses we have for these instruments?
How are we able to control these instruments?
What other hand-held tools and gauges do we use for production processes?
How do we make proper repairs and adjustments to production equipment before we put it into service?
How do we ensure that set-up meets process requirements and product specifications?
How can we make sure that “first piece” and “production runs” meet specifications?
How do we document set-up procedures so that they are accurate and suitable for repeatability?
How do we ensure that set-up meets ergonomic and other health, safety, and environmental standards?
How do we ensure that set-up meets equipment specifications?
88/88